## Slide 1: Biomedical Signal Processing 2018-2019 Autumn Introduction
Lecturer: Janka Hatvani Responsible lecturer: Dr. Miklós Gyöngy

## Slide 2: Biomedical Signal Processing 01 - Introduction
Today’s goal
BSP - An introduction
Course learning outcomes
Discussion of the Syllabus

## Slide 3: BSP – An introduction
Examples of biomedical signals
Use of biomedical signals
Instrument design aspects
Processing of biomedical signals
Notes: Take a look around in the classroom. Can you notice any biomedical signals beeing recorded? Sensitive information, be aware with health apps. (Android against GDPR?)

## Slide 4: Examples of biomedical signals
Which signals can be measured on these sites?

## Slide 5: Examples of biomedical signals
Biochemical
  Hormones
  Neurotransmitters
  Blood sugar level, …
Electrical
  ElectroNeuroGram
  ElectroCardioGram
  ElectroEncephaloGram
  ElectroMyoGram
„Physical”
  Temperature
  BloodPressure
  PhonoCardioGram
  PulseOximetry
  PhotoPlethysmoGraph

## Slide 6: What can the measurements be used for?
Notes: Diagnosis
Gaming
Rehabilitation
Fitness monitoring,
BCI
Intesive Care Unit
+basic research

## Slide 7: ECG - electrocardiography
Notes: Where do we want to measure it?
In the ICU for monitoring
In the gym/hospital for stress test
When a diagnosis has to be made (heart failures)
Heart Check PEN – for home use, if a failure is suspected (http://www.theheartcheck.com/consumer.html)
In an automated defibrillator
Pathologies of interest (all classed as arrhythmia):
- tachycardia (faster)/brachycardia (slower)
ectopic beats (Premature ventricular/atrial contraction, PVC/PAC)
conduction block (AV, left/right bundle branch block)
myocardial ischemia/infarction
atrial/ventricular flutter/fibrillation
Sudden cardiac death: ventricular arrhythmia (tachycardia)  ventricular fibrillation

## Slide 8: EEG - electroencephalography
Emotiv Video
Neurosky
NeuroCap
Notes: https://www.youtube.com/watch?v=bposG6XHXvU Sleep analysis / stage detection
Brain-computer interface (even reconstruction of speech)
Epilepsy detection (hospital—sometimes provoked, ambulatory), prediction
Pathologies of interest:
{In/Hyper/Para}somnia, Cyrcadian Rhythm Disorder
Locked in syndrome
Epilepsy
https://www.mobihealthnews.com/content/new-approval-memorymd-preparing-distribute-its-wearable-eeg-system
http://www.emotiv.com/apps/epoc/299/, http://a.tgcdn.net/images/products/zoom/eed1_neurosky_mindwave_mobile.jpg

## Slide 9: EMG - electromyography
from top: epimysial stimulating electrode, intramuscular stimulating electrode, epimysial recording (bipolar) electrode, spiral nerve cuff electrode
Notes: Diagnosis of neuro-muscular function
Kinesiology (study of movement)
Prosthetic control / rehabilitation
Human-Computer Interface
Pathologies of interest:
Muscular dystrophy
Peripheral Neuropathy
Muscle Inflammation
Pinched Nerve
Amyotrophic lateral sclerosis (ALS)
Myasthenia gravis (MG)
Carpal tunnel and related nerve compressions
http://www.elsevier.es/es-revista-revista-andaluza-medicina-del-deporte-284-articulo-surface-electromyography-why-when-how-X1888754611201253
https://www.nrsign.com/monopolar-vs-bipolar-emg-readings/
http://duinopeak.com/store/index.php?route=product/product&product_id=124
http://www.milmedtek.se/files/img/emg_messanordnung_beine600.jpg http://fescenter.org/about-fes-center/fes-center-facilities/technical-development-laboratory/

## Slide 10: Phonocardiography
ViScope
Notes: „Digital stethoscope”
Heart sound splitting
Heart murmurs
Fetal cardiography
Pathologies of interest:
atrial/ventricular septal defect, patent ductus arteriosus,
aortic/pulmonary stenosis, mitral/aortic insufficiency/regurgitation,
RBBB
http://www.thinklabs.com/
http://www.pentavox.hu/index.php/termekeink/fetaphon
https://www.dicardiology.com/product/new-visual-stethoscope-demonstrated-himss-2015

## Slide 11: Pulse Oximetry
Notes: Demonstration on smartphone/smartwatch Patient’s oxygenation
hospital monitoring (operating room, recovery room, ICU)
hospital/ambulatory diagnosis
Pathologies of interest:
hypoxemia  tissue hypoxia
sleep disorders: apnea/hypopnea
pulmonary disease: chronic obstructive pulmonary disease, asthma, community-acquired pneumonia
http://en.wikipedia.org/wiki/Pulse_oximetry, http://www.ncbi.nlm.nih.gov/pmc/articles/PMC3080222/
https://www.fitbit.com/eu/home
https://newsarchive.heart.org/dozens-of-babies-saved-after-pulse-oximetry-screenings/

## Slide 12: Blood pressure
Notes: Invasive hospital monitoring
Noninvase hospital diagnosis, ambulatory monitoring
Pathologies of interest:
systolic/diastolic {hypo/hyper}tension
brachycardia/tachycardia
stenosis
http://www.tensiomed.com/pictures/arg1.jpg, http://www.meditech.hu/images/stories/cikk_kepek/blue_bp_05_3.png, http://inventures.eu/sites/default/files/optoforce_photo1.jpg

## Slide 13: Multiple Signals
Notes: Hospital monitoring
Ambulance monitoring
Home monitoring/alarm system
Sport/fitness centers
Nursing home
Pathologies of interest:
arrythmia
acute renal failure
sepsis
http://www.innomed.hu/dynamic/innocare_s.pdf, http://www.innomed.hu/innocare_pico_hun

## Slide 14: Instrument design aspects
Stable, continuous measurement
Real-time measurement in many applications
Minimally invasive or non-invasive
Patient safety
Suitable SNR – from the power line interference, thermal noise  filtering
Interactions between different biomedical signals  filtering

## Slide 15: Processing of biomedical signals
filtering (denoising)
signal genesis + transduction
event detection
feature extraction
(dimension transformation and reduction)
classification and diagnosis
Notes: at the end of the day, interested in classification/diagnosis
what is that saying? is our body functioning normally or has it been modified by something
so we look for relevant features or parameters that could be telling us something relevant. Examples: heart rate
For that we need a biomedical signal from which to extract that
For this we need to collect the signal in some way, and we also need to understand how that signal arises
So we went back the way from diagnosis to signal collection. Now let’s go forward.

## Slide 16
 |  | Lecture title | Description | Lab tasks
10-Sep | 1 | Introduction | What is BSP? The syllabus | Physionet, Basic operations on datalines, Test
17-Sep | 2 | Signal Genesis | Understanding the physical background of PCG, BP, PO, PPG, ENG, ECG, EEG, EMG | Bloodpressure measurement techniques, modulation of a respiratory signal, body temperature of a corpse - DE
24-Sep | 3 | Genesis Equations | Mathematical model for the biomedical signals: single and coupled linear/non-linear oscillators | Solving higher order DEs in matlab. Comparison of the Fitzhug-Nagumo and Hodgkin-Huxley models
1-Oct | 4 | Noise Filtering | Noise types and different filters (synchronized averaging, ad-hoc, Wiener, adaptive) | Filtering competition: comparing different methods through removing undesired components from an ECG signal.
8-Oct | 5 | Event Detection | What events can interest us? The classical event-detection pipeline: filtering, envelope detection, decision rules | Implementation of a classical QRS detection method (Pan-Tompkins or Hamilton-Tompkins) and comparing it with a state-machine method.
15-Oct | 6 | Spectral Estimation | Comparison of Fourier spectrum, AR models and point-processes | FFT-issues: a reason for other spectral estimation techniques. Implementation of the AR-method, and learning about its usage.
5-Nov | 7 | Wavelets -1 | Spectrogram, Time-frequency uncertainty, from Gabor-wavelets to Continuous Wavelet Transform | Implementing and testing spectrogram calculating methods and understanding the time-frequency uncertainty through them.
12-Nov | 8 | Wavelets -2 | Discrete Wavelet Transform. Overcomplete bases, orthogonality, multiresolution analysis, wavelet filtering | Extracting the P300 from the measured signal. (Including spectrum-based noise filtering, event detection, synchronized averaging.)
 |  | EEG measurement | Measuring the P300 evoked potential | 
19-Nov | 9 | Sparsity | Definition and importance of sparsity. Sparsity promoting regulizers (lp norm, TV, Tikhonov). Solution of regularized problem (Soft-thresholding, Matching Pursuit, ADMM) | Decomposition of an EEG signal into Haar-wavelets, with Soft thresholding/Matching Pursuit as sparsity promoting methods
26-Nov | 10 | Source Separation | The source separation problem. Principle and Indeendent Compnent Analysis (PCA/ICA). | Separation of the heart sounds
 |  |  | Measuring the PCG signal | 
3-Dec | 11 | Classification | Computer Aided Diagnosis. Classification techniques - rule based method, Bayesian method, Cost Matrix | Preparation for the exam
10-Dec | 12 | Exam |  | 
Break on 22th, 29th October!!!

## Slide 17: Course Learning Outcomes
How do we connect to other courses?
How is it connected to your degree?
Why is it useful (even if you are working at a different field)?

## Slide 18: Syllabus

## Slide 19: Basic Information
Lecturer: Janka Hatvani
Office location: SOUND lab, room 204 (by the library)
(You can usually find me here)
Email: hatvanijanka@itk.ppke.hu
Responsible lecturer: Miklós Gyöngy
Office location: SOUND lab, room 204 (by the library)
(Monday and Tuesday)
Email: gyongymiklos@itk.ppke.hu

## Slide 20: The plan (schedule available on Wiki)
11 lectures, Mondays 10:15-12:00, Neumann hall
11 labs – group 1: Mondays 16:15-18:00 (classroom 422) – group 2: Tuesdays 8:15-10:00 (classroom 220) – group 3: Fridays 12:15-14:00 (classroom 219)
10 group-assignments during lab, report to be handed in through hatvani.janka@itk.ppke.hu, before the day of your next lab - g1: Sunday 24:00, g2: Monday 24:00. g3: Thursday 24:00
Written exam: 10 December

## Slide 21: Assessment
To get a grade:
Attend as many lectures/labs as required by Faculty Rules
Sit end-of-year written exam
Grade Calculation:
50 points from the 10 reports
50 points for the exam
extra points for answers at class (max. 1/lecture)
points | 39- | 40-53 | 54-67 | 68-81 | 82+
grade | 1 | 2 | 3 | 4 | 5

## Slide 22: Literature
Primary Course book:
Rangayyan: Biomedical Signal Processing: A Case-Study Approach. In library. Electronic copy
Also useful:
Sörnmo and Laguna: Bioelectrical Signal Processing in Cardiac and Neurological Applications. In library.
Webster (ed.): Medical Instrumentation: Application and Design
Lecture slides will be available on Wiki after each class Always check the Notes of the slide ↓
Notes: Yes, here will be the useful information  https://memegenerator.net/img/instances/52069451/very-information-much-useful.jpg